## Slide 1
1
P. RAMANJANEYA PRASAD
Department of Electronics

## Slide 2
2
+1
=3
HOW THE COMPUTER GETS THE ANSWER

## Slide 3
A computer understands
information composed of only zeros and ones.
The decimal number system is convenient for the programmer.
The computer uses binary digits for its operation.
0
1
0
1
1
0
1
1
0
0
1
0

## Slide 4: DECIMAL
BASIC NUMBER SYSTEM
HEXA DECIMAL
OCTAL
BINARY
4

## Slide 5: DIGITS
DECIMAL NUMBER SYSTEM
0,1,2,3,4,5,6,7,8,9.
10
BASE
5

## Slide 6: 4*103
DECIMAL NUMBER 4598
6
9*101
8*100
5*102

## Slide 7: 0,1
BINARY NUMBER SYSTEM
DIGITS
•2
BASE
7

## Slide 8: 1*23
BINARY NUMBER 1011
1*21
1*20
8
0*22

## Slide 9
HEXADECIMAL NUMBER SYSTEM
0,1,2,3,4,5,6,7,
8,9,A,B,C,D,E,F.
DIGITS
16
BASE
9

## Slide 10: HEXADECIMAL NUMBER 1A5D
5*161
D*160
10
A*162
1*16 3

## Slide 11: DIGITS
OCTAL NUMBER SYSTEM
0,1,2,3,4,
5,6,7,8.
•8
BASE
11

## Slide 12: 5*83
OCTAL NUMBER 5273
7*81
3*80
12
2*82

## Slide 13: CONVERSIONS IN BASIC NUMBER SYSTEM
13

## Slide 14: BINARY TO DECIMAL
1 0 1 0 1
BINARY
BIT
POSITION
5 4 3 2 1
MUL WITH BASE
21
DECIMAL
14
1*24+0*23+1*22
+0*21+1*20.

## Slide 15: HEXADECIMAL TO DECIMAL
5A9
HEX
BIT POSITION
3 2 1
DECIMAL
1449
15
5*162
+A*161
+9*160
MUL WITH BASE

## Slide 16: OCTAL TO DECIMAL
645
OCTAL
BIT
POSITION
3 2 1
MUL WITH
BASE
DECIMAL
421
16
1
6*8 2+4*8
+5*8.0

## Slide 17: DECIMAL TO BINARY
Q=19
R=1
39
Q=9
R=1
19
Q=4
R=1
9
Q=2
R=0
4
Q=1
R=0
2
Q=0
R=1
1
17
LSB
MSB
Divide through out by 2
DECIMAL = 39
BINARY = 100111

## Slide 18
DECIMAL TO HEX
Q=2
R=3
35
Q=0
R=2
2
18
Divide through out by 16
LSB
MSB
DECIMAL = 35
HEX = 23

## Slide 19: DECIMAL TO OCTAL
Q=57
R=5
461
Q=7
R=1
57
Q=0
R=7
7
19
Divide through out by 8
LSB
MSB
DECIMAL = 461
OCTAL = 715

## Slide 20: BINARY TO HEXADECIMAL
BINARY
4BITS DIV
(0101)(1101)(1001)
HEX
(010111011001)2
20
(5) (D) (9) =(5D91)6

## Slide 21: BINARY TO OCTAL
BINARY
3BIT DIV
(101)(111)(100)
OCTAL
(101111100) 2
21
(5) (7) (4)
=(574)8

## Slide 22: HEXADECIMAL TO BINARY
EXPANSION
(0101)(1100)
HEX
(5C) 16
22
BINARY
(01011100) 2

## Slide 23: OCTAL TO BINARY
OCTAL
EXPANSION
(100)(011)
BINARY
(436) 8
23
(100011) 2

## Slide 24: HEXADECIMAL TO OCTAL
HEX
(0100)(1101)(1111)
EXP
BINARY
(010)(011)(011)(111)
3BIT DIV
OCTAL
24
(4DF)16
(010011010000)2
(2337)8

## Slide 25: OCTAL TO HEXADECIMAL
OCTAL
(100)(101)(110)
EXP
BINARY
(0001)(0010)(1110)
4BIT DIV
HEX
25
(456) 8
(100101110)2
(12E) 16

## Slide 26: REPRESENTATION OF NEGATIVE NUMBER
9’S & 10’S COMPLIMENT
DECIMAL NUMBER SYSTEM
1’S & 2’S COMPLIMENT
BINARY NUMBER SYSTEM

## Slide 27: BINARY ARITHMETIC
1
BINARY ADDITION
2
BINARY SUBTRACTION

## Slide 28: BINARY ADDITION
0 + 0 = 0
1 + 0 = 1
0 + 1 = 1
1 + 1 = 0 1 (Carry bit)
1 1 0 1
+0 0 0 1
1 1 1 0
(13 decimal)
(+1 decimal)
(14 decimal)

## Slide 29: BINARY SUBTRACTION
0 ‐ 0 = 0
1 ‐ 0 = 1
0 ‐ 1 = 1 1 (Carry bit)
1 ‐ 1 = 0
1 1 0 1
+ 0 0 1 1
1 0 1 0
(13 decimal)
(-3 decimal)
(10 decimal)
Borrow
29

## Slide 30: SIGNED ARITHMETIC OPERATION
30
MSB bit is reserved to represent the sign of
the number.
When the number is negative, the sign bit is kept one.
When the number is positive, the sign bit is 0.
In 8-bit processor, MSB = sign bit & other 7
bits = number.
In 16-bit processor, MSB = sign bit & other 15 bits = number.

## Slide 31: EXAMPLES
0 0 0 0 0 1 0 1 (+5 decimal)
0 0 0 0 0 1 0 0 (+4 decimal)
0 0 0 0 1 0 0 1 (+9 decimal)
0 0 0 0 0 1 0 1 (+5 decimal)
1 0 0 0 0 0 1 0 (-2 decimal)
1 1 1 1 1 1 0 1 (1’comp of -2)
0 0 0 0 0 0 1 1 (+3 decimal)
1
1 1 1 1 1 1 1 0 (2’s comp of -2) 2
1
2
1

## Slide 32: BCD AND GRAY CODE

## Slide 33: LOGIC GATES
35
Logic gates perform basic logical functions.
They are fundamental building blocks of digital integrated circuits.
Most logic gates take an input of two binary
values, and output a single value of a 1 or 0.
Some circuits may have only a few logic gates, while others, such as microprocessors, may have millions of them.
There are seven different types of logic gates, which are outlined.

## Slide 34
36

## Slide 35
35

## Slide 36
36

## Slide 40
40

## Slide 41: Thank you
44
For any clarifications on the topics you can email to prasadelectronics@avanthi.edu.in